ALSA
(Advanced Linux sound architecture )
- Part of the linux kernel while audio pulse is the middleware
- Sound card device driver creation
- Device driver for that card also available
- Data passing through the audio jack or speaker is in analog form
- Each sound card have DSP as built-in processing unit and its function is to ADC and DAC conversion
- Soundcard have its own memory to store information now a days ( buffer cache )
- Soundcard without DSP and memory will use CPU utilisation and main memory
- It supports all interface
- Fully modularized driver
- SMP and thread safe design
- User space libraries
- Support for OSS API's
- Responsible for translating your hardware capabilities into software API's
- It mixes games and music ( two audio pulse into single and play )

read this page about ALSA Driver creation
http://www.alsa-project.org/~tiwai/writing-an-alsa-driver/
http://www.alsa-project.org/main/index.php/Main_Page
we will get enough knowledge

ALSA File Tree Structure
Go to linux source directory /usr/src/$(uname -r)/sound
sound
                /core
                        /oss
                        /seq
                                /oss
                                /instr
                /ioctl32
                /include
                /drivers
                        /mpu401
                        /opl3
                /i2c
                        /l3
                /synth
                        /emux
                /pci
                        /(cards)
                /isa
                        /(cards)
                /arm
                /ppc
                /sparc
                /usb
                /pcmcia /(cards)
                /oss

API's
Application uses ALSA interface in order to get the services by the ALSA
Information interface	-> /proc/asound
Control interface	-> /dev/snd/controlCX
Mixer interface	-> /dev/snd/mixerCXDX
PCM interface	-> /dev/snd/pcmCXDX
Raw MIDI interface	-> /dev/snd/midiCXDX
sequencer interface	-> /dev/snd/seq
Timer interface	-> /dev/snd/timer