Multimedia Fundamentals
Keertikumar A
Bharath P
Ashwini H P

---
Contents
- Introduction to Multimedia Framework.
- Android Multimedia Framework.
- Gstreamer Framework.
- Video Codec.

---
Introduction to Multimedia Framework
- Multimedia Framework is software framework that handles media on computer and through network.
- A good Multimedia Framework offers a modular architecture to easily support for new audio, video, container formats and for Transmission protocols also.
- Examples :
  1. Gstreamer Framework
  2. Direct Show
  3. Quick Time

---
Android Multimedia Framework

---
- At the native level, Android provides a multimedia framework that utilizes the Stage-fright engine for audio and video recording and playback.
- Stage-fright comes with a default list of supported software codecs and you can implement your own hardware codec by using the OpenMax integration layer standard.
- The OpenMax IL provides a standardized way for Stage-fright to recognize and use custom hardware based multimedia codecs called camponents.

---
Big Picture of Stage-fright Engine

---
Stage-fright Work flow

---
Gstreamer
Gstreamer is a pipeline based multimedia framework.
Why using Gstreamer?

---
Overview
Gstreamer Framework uses plugin architecture.
Plugins can be linked and arranged in a pipeline.

---
Gstreamer Building Blocks
Element:
The states of element are.,
  - null: no resource is allocated
  - ready: resources are allocated, but the streams are not opened
  - pause: streams are opened but no processed
  - play: streams are being processed
Each element can change state during the execution of application.

---
Continued.,
Bin:
Bin is an element which contains other elements.
Since it is an element it can have the same states as mentioned for element.
Pad:
The pads are element's interface. Streams flow from an	element's source pad to another element's sink pad.

---
Continued.,
Buffers: They can pass streaming data between elements in the bin.
Events: Objects used to notify elements which are waiting for a particular event to occur.
Message: Objects posted on pipeline bus to notify the application of any particular information(bugs,state changes,end of streams).
Query: Objects sent from application or between elements to ask a particular information(duration, positions, etc.,).

---
Video Codec
- RGB and YUV formats.
- Video codec:
  - Video encoding
  - Video decoding

---
RGB and YUV format
RGB :
  - RGB color space or RGB color system, constructs all the colors from the combination of the Red, Green and Blue colors.
  - The red, green and blue use 8 bits each, which have integer values from 0 to 255. This makes 256*256*256=16777216 possible colors.
YUV :
  - YUV is a way of breaking the brightness and colors in the image down into numbers.
  - Y → Luminance and UV → Chrominance

---
RGB and YUV format
- Most cameras take the light coming into the lens, and convert that into 3 sets of numbers, one for Red, one for Green, and one for Blue(RGB).
- If we need to lower the brightness uniformly on an image, we need to do it to all 3 colors. There’s also a LOT of redundancy in the data.
- To solve this there we need to convert from RGB to YUV.
- Which breaks the signal down into a Y, or luminance component, and 2 components that store color info without brightness info – a Blue component and a Red component that don’t contain any brightness.

---
Video codec
- The process of compression involves applying an algorithm to the source video to create a compressed file that is ready for transmission or storage(encoder).
- To play the compressed file, an inverse algorithm is applied to produce a video that shows virtually the same content as the original source video(decoder).
- A pair of algorithms that works together is called a video codec (encoder/decoder).
- Video compression standards are, Motion JPEG, MPEG-4 Part 2 (or simply referred to as MPEG-4) and H.264. H.264 is the latest and most efficient video compression standard.

---
Video encoding

---
Video decoding